## Slide 1: Condition Monitoring of Structures, Machines and Processes
Tutorial

## Slide 2
Matlab:
Data Processing
2

## Slide 3: Exercice 14.1
Pre-processing Signals and Data Reduction
Task:
Download the files Gear1_1e5.mat and Gear3_1e6.mat and load them into your MatLab workspace. The files correspond to recordings of structure borne noise signals of a bicycle hub in gear 1 and gear 2 with a sampling frequency of , respectively.
Reduce the data of gear 3 to fit the sampling frequency of gear 1
  Hint: Use the command resample() or work with the colon operator : as in A(1:2:end)
Plot the data in two different plots.
Determine the average and the root mean square of the amplitude of the signals.
Advanced: Plot and interpret the frequency spectrum of each plot.
  Hint: Use the fft command or the app signal analyzer initialised by executing the command signalAnalyzer.
  Determine the peak frequency, that is, the frequency of highest magnitude in the FFT-plot.

## Slide 4: Exercice 14.2
Classification
Task:
The file GearX_1e5.mat is a recording of the bicycle hub in an unknown gear.
  Based on the results of exercise 14.1 try to determine the gear.